Here is the list of the parameters in the input file:

"type" indicate the type of the particle, "0" means proton, "1" means electron, "2" means Au;
"csv_out" control the output of csv file;
"dynamicOn" control the behavior of the beam dynamic at the beginning of the time, default is “off”;
“turn_start” legacy parameters, starting number of the turn, just set it to “0”;
“mainRF” the index of the RF used by the code to calculate ramping of Vref and Iref;
“main_detune” the index of RF used by the code to calculate ramping of the detuning;
“R”, the radius of the ring;
“GMTSQ”, the gammaT^2;
“Gamma”, the reference gamma of the beam;
“nBeam”, the number of beams;
“beam_shift”, the shift between two beams in unit of mainRF cycle;

“n_turns”, total number of turns the code with run;
“n_dynamicOn”, the number of turn we turn on the beam dynamics;
“n_bunches”, the number of bunches in one beam;
“n_fill”, the turn we start to ramp the bunches charge;
“n_q_ramp”, the number of turns it takes to ramp the charge;
“n_detune_start”, the turn we start to ramp the detuning;
“n_detune_ramp”, the legacy parameter, not real in use;
“n_detune_ramp_tot”, the turn we finish the ramping of the detuning;
“n_I_ramp_start”, the turn we start to ramp the driving current of the RF amplifier;
“n_I_ramp_end”, the turn we finish ramping the driving current of the RF amplifier;

“Prad”, the radiation power of the beam, in unit of watts. We need to compensate it with the RF voltage;
“t_rad_long”, the longitudinal radiation damping time, in unit of seconds;
“Ek_damp”, the artificial damping on the bunch energy before the bunch is rampped to full charge, in unit of number of synchrotron oscillation;
“Ek_damp_always”, the artificial damping on the bunch energy after the bunch is rampped to full charge, in unit of number of synchrotron oscillation;
“Npar”, number of macro particles in one bunch;
“NperBunch”, the nubmer of real particles in one bunch;
“N_bins”, the number of time slices per RF cycle;
“fill_step”, the number of RF cycles between bunches;
“siglong”, the sigma gamma;
“A”, the 95% particle emittance, assuming Gaussian bunch;

“nRF”, number of RF systems;
“nRF1”, number of RF systems in ring 1;
“nRFc”, number of RF systems shared by both rings;
“nRF2”, number of RF systems in ring 2;
“nHOM”, legacy parameters, not in use;

“nCav”, array type parameters, indicate the number of cavities for each RF system, length of the array should be equal to “nRF”;
“h”, array type parameters, the harmonic numbers of each RF systems;
“RoQ”, array type parameters, the R over Q of each RF systems, circuit definition;
“I_Q_ref_ini”, array type parameters, the initial values of the the Q component of the reference driving current;
“I_Q_ref_final”, array type parameters, the final values of the the Q component of the reference driving current;
“I_I_ref_ini”, array type parameters, the initial values of the the I component of the reference driving current;
“I_I_ref_final”, array type parameters, the final values of the the I component of the reference driving current;
“Iref_I”, array type parameters, the values of the the I component of the reference driving current, should be equal to “I_I_ref_final”;
“Iref_Q”, array type parameters, the values of the the Q component of the reference driving current, should be equal to “I_Q_ref_final”;
“Vref_I”, array type parameters, the I component of the reference cavity voltage;
“Vref_Q”, array type parameters, the Q component of the reference cavity voltage;
“detune”, the initial detune of each RF system, in unit of Hz;
“detune_ini”, the initial detune of each RF system;
“detune_mid”, legacy parameter, the mid point of the detune;
“detune_final”, legacy parameter, the final value of the detune of each RF system;

“delay”, array type parameters, the delay for each direct feedback system, not really properly implemented yet;
“n_fb_on”, array type parameters, the turn we turn on the direct feedback;
“gII” to “gQIi”, the gains of the direct feedback, the integral part is not implemented;
“PA_cap”, the cap of the power amplifier, not implemented;
“epsilon_comb”, the epsilon of the comb filter;
“g_comb”, the g number of the comb filter;
“QL”, loaded Q of each RF system;

“n_ini_CBI”, the number of coupled bunch modes to initialize;
“mu”, the mus of the coupled bunch mode;
“CBI_ini_amp”, the amplitudes of the coupled bunch modes, in unit of gamma;